## Slide 1: INTRODUCTION
01
Energy
Increasing energy consumption of main memory.
Limitation of scalability
02
New materials
Application of non-volatile material
phase change random access memory (PCM)
03
Architecture
Proposed hybrid main memory architecture
Notes: With the development of multi-core system and big data application, computer system is becoming more and more data-centric. Consequently, large capacity memory is demanded in order to improve the data processing performance. However, the traditional DRAM based memory faces the limitation of both scalability and energy consumption due to its inherent physical properties and charging work mechanism.
Researches show that the DRAM-based main memory accounts for 40% of the total energy consumption of modern computer systems.
Phase Change Memory (PCM) is one of the most promising and rapidly developed technologies, which is byte addressable, higher density (has the potential to scale down to 5nm [5]), lower power consumption and has nanosecond range access time.
Many researchers have put forward the idea of design main memory architecture with both DRAM and PCM. Some studies suggest to use a small DRAM as an upper-level buffer for the main memory of only PCM. On the other hand, there also have been some work on having parallel PCM and DRAM which constitute the unified main address space.

## Slide 2: INTRODUCTION
Advantage
High density
Power-economy
Non-volatile
Shortage
High
Write-power
Slow
write
Limited
endura-nce
PCM
Notes: 相比较于传统传统DRAM内存，NVM具有密度大、静态功耗小、掉电非易失等特点。
然而，任何事物都具有两面性，NVM同样存在着明显缺点，如写功耗大，写延迟长，寿命有限等
Compared to DRAM, PCM typically has better power efficiency due to low background power and absence of refresh energy consumption. However, current NVM technologies such as PRAM usually suffer from low write endurance, as well as high write latency and power consumption. For instance, a detailed comparisons between DRAM and PRAM are shown in NEXT slide.

## Slide 3: INTRODUCTION
 | Non- Volatile | Density | Speed (Latency) | Dynamic Power (nj/b) | Leakage Power (W/GB) | Write Endurance
PCM | Yes | Very High (4X DRAM) | Fast Read(20ns) Slow Write(150ns) | Low Read(0.2) High Write(1.0) | Low (0.05) | 
DRAM | No | Medium | Fast(15ns) | Medium(0.1) | High (1.3) | unlimited
 | Non- Volatile | Density | Speed (Latency) | Dynamic Power (nj/b) | Leakage Power (W/GB) | Write Endurance
PCM | Yes | Very High (4X DRAM) | Fast Read(20ns) Slow Write(150ns) | Low Read(0.2) High Write(1.0) | Low (0.05) | 
DRAM | No | Medium | Fast(15ns) | Medium(0.1) | High (1.3) | unlimited
Notes: As shown in this table, PCM has some advantages such as Non-volatile, very high density and very low leakage power. But we could not ignore these disadvantages such as slow write, high write power and lower write endurance.

## Slide 4
High
Speed
low
power
High
density
High
density
low
power
High
Speed
Hybrid of DRAM and PCM
INTRODUCTION
Notes: 那么，怎样才能同时利用DRAM和NVM的优点来构造大容量，高速度，低功耗的主存呢？
国内外学术界提出混合主存架构—下一页PPT
In order to get a optimized memory system as high density, high speed and low power, we mix DRAM and PCM as memory, use the hybrid memory of DRAM and PCM which is shown in the left diagrammatic drawing.

## Slide 5: PROBLEM ANALYSIS
The novel policy
Traditional algorithms
Put the read page into PCM.
Put the write page into DRAM.
Put the write page into DRAM.
To make the utmost of DRAM.
x1
PCM
DRAM
write
read
x1
x2
Seek DRAM for X1.
If DRAM has free space
Seek DRAM for x2;
x2
Else
Seek PCM+DRAM for x2;
x2
Notes: Base tradition method, we hope all the read operations best placed into PCM and all the write operations on DRAM in order to guarantee the write
Endurance of PCM.
In our design, more write operations will be on DRAM. Specifically, to make the utmost of DRAM, we put more operation on DRAM whether it is write or read operation. Because the static energy consumption is relatively constant, so allocating active page on DRAM is very sensible if there is free space in DRAM.
For example, x1 is a write page, it will be put into DRAM. X2 is a read page, if DRAM has free space, it will be assigned into DRAM. Otherwise, it will be sent to PCM.

## Slide 6: PROBLEM ANALYSIS
Set X to be candidate
Write to X
The novel policy
Traditional algorithms
Migrate the read-intensive page from DRAM to PCM.
Migrate the write-intensive page from PCM to DRAM.
Migrate the write-intensive page from PCM to DRAM.
Increase the migration threshold to avoid the bad migration.
x
PCM
DRAM
Sequential Write
Migrate
x
Notes: In traditional methods, all the read-intensive pages will be migrated from DRAM to PCM, and the write-intensive page will be migrated from PCM to DRAM. But it is very difficult that how to judge the page is read-intensive or write-intensive. So it makes more bad migration.
(the first) When a page originally in PCM is migrated to DRAM and then back to PCM without being written enough times while in DRAM.
(the second) When a page originally in DRAM is migrated to PCM and then back to DRAM with too many write accesses while in PCM.
In our paper, we only consider that the write-intensive is migrated from PCM to DRAM. We do not migrate the read-intensive from DRAM to PCM for making full advantage of DRAM. Specially, we increase the migration threshold to avoid the bad migration.
For example, page x is in PCM and its dirty bit is 1. if a write operation to X happens, the page X is set to be candidate, until an another write operation coming, the migration will be run.

## Slide 7: PROBLEM ANALYSIS
The novel policy
Traditional algorithms
Evict the least recently used page.
Evict the least recently used page.
Reduce the probability of re-loaded page to be evicted.
PCM
DRAM
x
y
Search around PCM and DRAM by LRU
z
Search around DRAM:
if y is a re-loaded page
skip and set it to be candidate
Else
evict y
x
write-intensive
Unknown features
Notes: In traditional methods, while the page is fault, the least recently used page is always evicted firstly.
In our paper, according to the principle of locality, we also need to consider the schedule history of being evicted page.
For example, if X is a new page, it will be sent into PCM or DRAM. If X has been used and the write-intensive bit is one, it will be sent into DRAM.
The method will search around DRAM for an suitable page space by LRU. Although the page Y is suitable by LRU, but it is a re-loaded page, so we skip it and set it to be candidate.

## Slide 8: CLOCK-HM ALGORITHM
reference bit
second chance bit
CLOCK List: CL
History LRU List: HLL
R-write bit
W-intensive bit
W-intensive bit
Hdram searches around DRAM
Hrep searches around PCM+DRAM
Notes: CLOCK-HM is based on traditional CLOCK algorithm to manage pages in hybrid page but adds additional metadata for each page and history list to record the history page cache reference.
As shown in this slide, we maintain two list: clock list CL and history LRU list HLL. And employ four flag bits to manage the cache: reference bit denotes whether the page was accessed or not , second chance bit denotes whether the page has been re-loaded, R-write bit denotes the page has been written more than twice, W-intensive bit shows whether this page is a write intensive page or not.
And the pointer of Hdram is used to searche around DRAM, and the hand of Hrep is used to search around the whole memeory, include both DRAN and PCM.

## Slide 9: CLOCK-HM (page x, operation op)
 | P/D | reference bit | second chance bit | R-write bit | W-intensive bit
P1 | 1 | 0 | 0 | 0 | 0
P2 | 1 | 1 | 0 | 1 | 0
P3 | 1 | 1 | 0 | 1 | 1
D1 | 0 | 0 | 0 | 0 | 0
D2 | 0 | 1 | 0 | 1 | 0
X |  |  |  |  | 1
Y |  |  |  |  | 
P1
P2
P3
•••
•••
•••
•••
PCM
DRAM
D1
D2
•••
•••
•••
Read P1
1
Read D1
1
Write P2
Write D2
1
1
Write P3
Call Migrate
Write X
Read Y
Call Replace
Notes: Now, we describe our method in detail by a animation.
We assume that pages p1,p2,p3 in PCM and d1,d2 in DRAM. The table is the status of each page in LIST CL.
While read p1 and p2, modify the reference bits.
While write p2 and d2, modify the w-intensive bits because the r-write bits have already been one.
While write p3, for w-intensive bit has been one, so it triggers the migration from PCM to DRAM.
While write x or read y, x and y are not in memory, page fault happen. So it triggers page replacement.

## Slide 10: Page Migrate
P3
P3
 | P/D | reference bit | second chance bit | R-write bit | W-intensive bit
P3 | 1 | 1 | 0 | 1 | 1
0
Search around by Hdram
Evict E and record E in HLL
Migrate P3 to E of DRAM
P1
P2
•••
•••
•••
•••
D1
D2
•••
•••
•••
DRAM
PCM
P3
Write P3
Migrate(P3)
Notes: A write operation on page P3, this page is write-intensive and is in PCM, so it triggers the migration from PCM to DRAM.
First, the pointer Hdram searches around LIST CL and modifies the flag bits of each passed page concurrently as shown in this slide.
Second, find the suitable page E, so evict it and save the flag into LIST HLL.
Third, Migrate P3 to E of DRAM.

## Slide 11: Page Replace (TYPE = DRAM or NULL)
 | P/D | reference bit | second chance bit | R-write bit | W-intensive bit
X |  |  |  |  | 1
0
W-intensive is 1:
X is in HLL
Search around by Hdram
Evict E and record E in HLL
Replace X to E of DRAM
P1
P2
P3
•••
•••
•••
•••
D1
D2
•••
•••
•••
X
x
x
0
0
0
DRAM
PCM
Write X
Replace(DRAM)
Notes: A write operation for X, but page X is not in memory, it triggers Page Replace.
Firstly, searches around LIST HLL for giving a judgement that the page X is a new one or re-loaded.
Now, we assume page X is a re-loaded page and is write-intensive.
So, searches around CL by Hdram and modifies the flag bits of each passed page concurrently as shown in this slide.
To find the suitable page E, so evict it and save the flag into LIST HLL.
At the last, Replace X to E of DRAM.

## Slide 12: Page Replace (TYPE = DRAM or NULL)
 | P/D | reference bit | second chance bit | R-write bit | W-intensive bit
Y |  |  |  |  | 0
0
P1
P2
P3
•••
•••
•••
•••
D1
D2
•••
•••
•••
Y
0
0
0
0
Y is not in HLL
Search around by Hrep
Evict E and record E in HLL
Replace Y to E of PCM
Y
PCM
DRAM
Read Y
Replace( )
Notes: A read operation for Y, but page Y is not in memory, it triggers Page Replace.
Firstly, searches around LIST HLL for giving a judgement that the page X is a new one or re-loaded.
Now, we assume page X is a new one.
So, searches around CL by Hrep and modifies the flag bits of each passed page concurrently as shown in this slide.
To find the suitable page E, so evict it and save the flag into LIST HLL.
At the last, Replace Y to E of DRAM.

## Slide 13
原型设计过程简介
1
4
3
2
主要工作
提升访存速率
寻求硬件设计优化方案
分组并行
提升访存速率
优化混合控制器设计
多级分组阵列
探讨访存速率提升空间
寻求并行设计解决方案
并行设计
探究存储器件基础性能
积累硬件设计经验
性能探究

## Slide 14: 方案进程介绍
采用由浅及深、由单片到并行、由单级并行到多级阵列设计的方式对统一内外存原型进行设计和实现
方案一
方案二
方案三
方案四
方案五
基于FPGA的
PCM性能测试平台
基于ARM的
嵌入式混合
存储验证平台
基于DDR总线的统一内外存验证方案
通用计算机
统一内外存
验证方案
基于Zynq的
统一内外存
SOC验证方案
方案六
“统一内外存”
多级分组阵列
验证原型

## Slide 15: 方案说明
方案六：统一内外存验证原型
4路FPGA并行
12片MRAM并行

## Slide 16
统一混合主存原型展示
MRAM子板
主芯片：Spartan6 FPGA
3组4片共计12片MRAM并行
Zynq处理器
（ZynqXC7Z03）
利用FPGA实现混合存储控制器
底板
原型硬件展示
提供4个DIMM插槽
实现4块子板可并行

## Slide 17
读操作过程（768bits位宽）
原型读操作过程示意
读MRAM芯片数据
子板FPGA获取MRAM芯片数据
底板FPGA获取子板FPGA数据

## Slide 18
写操作过程
原型读操作过程示意
混合控制器编程
底板FPGA写指令传输至子板FPGA
子板FPGA写操作传输至MRAM芯片

## Slide 19: 原型演示展示
测试环境
一
测试方案
二
指标测试与对比
四
测试过程
三

## Slide 20: 2. 原型系统的测试方案
基准程序测试

## Slide 21: 2. 原型系统的测试方案
基于示波器的测试

## Slide 22: 2. 原型系统的测试方案
功率Pall=电压U*电流Iall
PMRAM=Pall- N *PFPGA N为子板数量
基于万用表的测试

## Slide 23: 3. 测试过程
基准程序测试
Chart: BenchMark读操作(1)
CRC | 2.056 | 2.0671 | 2.0565 | 2.0658 | 2.0642 | 2.0573
FFT | 2.0215 | 2.0186 | 2.0214 | 2.0269 | 2.019 | 2.0197
dijikstra | 2.067 | 2.0564 | 2.0675 | 2.0571 | 2.0668 | 2.0589
patricia | 2.019 | 2.0216 | 2.0155 | 2.0186 | 2.0176 | 2.0208
qsort_num | 2.025 | 2.018 | 2.0291 | 2.0272 | 2.0214 | 2.0242
Matrix_add | 2.085 | 2.079 | 2.0965 | 2.0741 | 2.092 | 2.0906
Matrix_mul | 2.0658 | 2.0605 | 2.0671 | 2.0665 | 2.0685 | 2.0713
Chart: BenchMark读操作(2)
| 1 | 2 | 3 | 4 | 5 | 6
BubbleSort | 2.0675 | 2.073 | 2.0692 | 2.0694 | 2.0659 | 2.0779
ChooseSort | 2.0798 | 2.0884 | 2.0915 | 2.0896 | 2.0928 | 2.0899
qsort_string | 2.0718 | 2.0692 | 2.0652 | 2.0729 | 2.0684 | 2.0661
BF_Match | 2.0612 | 2.0598 | 2.0567 | 2.064 | 2.0674 | 2.0657
KMP_Match | 2.0732 | 2.0642 | 2.0685 | 2.0697 | 2.0706 | 2.0667
Rand_Access | 2.0851 | 2.0919 | 2.0875 | 2.093 | 2.0899 | 2.0904

## Slide 24: 3. 测试过程
基准程序测试
Chart: BenchMark写操作(1)
| 1 | 2 | 3 | 4 | 5 | 6
crc | 1.9585 | 1.9596 | 1.9615 | 1.972 | 1.9644 | 1.963
fft | 1.9603 | 1.9503 | 1.9615 | 1.9624 | 1.9582 | 1.9632
dijikstra | 1.9623 | 1.9551 | 1.9604 | 1.9512 | 1.9591 | 1.9576
patricia | 1.9592 | 1.9653 | 1.9609 | 1.9646 | 1.9563 | 1.9612
qsort_num | 1.9669 | 1.9703 | 1.9592 | 1.9603 | 1.9652 | 1.9584
Matrix_add | 1.9596 | 1.9642 | 1.9702 | 1.9569 | 1.9664 | 1.9689
Matrix_mul | 1.964 | 1.9627 | 1.9586 | 1.9603 | 1.963 | 1.9574
Chart: BenchMark写操作(2)
| 1 | 2 | 3 | 4 | 5 | 6
BubbleSort | 1.9896 | 1.9742 | 1.9739 | 1.9812 | 1.9845 | 1.9867
ChooseSort | 1.9769 | 1.9877 | 1.9886 | 1.9742 | 1.9854 | 1.9835
qsort_string | 1.9723 | 1.9745 | 1.9768 | 1.9813 | 1.9694 | 1.973
BF_Match | 1.9592 | 1.965 | 1.9586 | 1.957 | 1.9627 | 1.9634
KMP_Match | 1.9642 | 1.9612 | 1.9579 | 1.963 | 1.9647 | 1.959
Rand_Access | 1.9678 | 1.9658 | 1.9692 | 1.9704 | 1.9765 | 1.9722

## Slide 25: 3. 测试过程
示波器测试
测试条件 |  | 读Δt (us) | 读速率（GB/s） | 写Δt (us) | 写速率（GB/s）
数据位宽（bit） | 数据大小 （KB） |  |  |  | 
768 | 240 | 114 | 2.0068 | 126 | 1.8604
768 | 240 | 114 | 2.0068 | 120 | 1.9022

## Slide 26: 3. 测试过程
万用表测试
状态 | 电压 | 电流 | 总功率 | 子板数量
读写 | 12V | 612mA | 7.344W | 4
空闲 | 12V | 300mA | 3.6W | 4

## Slide 27
指标内容 | 拟达到技术指标要求 | 实际技术指标
读操作平均速率 | 2GB/s | 2.0450 GB/S
写操作平均速率 | 400MB/s | 1.9808 GB/S
读写平均功耗 | <1W | 0.746W/子板
空闲平均功耗 | <0.5W | 0.429W/子板
4.指标测试与对比

## Slide 28: 测试方法-示波器

## Slide 29: 测试方法-基准测试程序

## Slide 30: 测试方法-万用表
功率Pall=电压U*电流Iall
PMRAM=Pall- N *PFPGA N为子板数量

## Slide 31: 总体设计方案
Notes: 实现DDR3接口、MRAM阵列管理、DRAM管理

## Slide 32: 阵列设计--分级控制
单级连接架构受引脚数目影响，无法实现高并行设计
多级连接架构可以有效的解决引脚瓶颈问题
Notes: 为实现较高的MRAM访存带宽，需要互联数十片MRAM芯片。每片MRAM需求的引脚数目约为38，48片MRAM互联的需求引脚数目需要达到1000根以上。目前，极少数的FPGA芯片用户IO数目可达到1000根以上，而且此类FPGA价格昂贵，外围电路更加复杂。考虑到MRAM单片数据访问速率约为25MHz，我们采用分级策略，第一级FPGA部署MRAM控制器，连接12片MRAM，约需要230根互连线，数据访问速率为25MHz。第二级，FPGA间采用更高频率（约140MHz）的数据访存时钟，从而实现以更少的互连线（约50根）实现需求的数据带宽。

## Slide 33: 阵列设计--分组设计
主要影响因素：
信号稳定性
FPGA驱动能力
采用分组设计策略：组内并行
组间并行
Notes: 组内并行，4片MRAM共享地址和控制线，数据线相互独立，使用扩展位宽的存储器控制方式。理论上，组内并行的MRAM数量越多，相同FPGA可以连接更多的MRAM，存储子板的数量可以更少。但是，考虑到FPGA信号线在高速翻转下的驱动能力，地址线和控制线所驱动的MRAM芯片数量设定为4片，采用有限的信号线实现多片MRAM的控制。
组间完全并行，每组MRAM读写通道完全独立，提供较大的灵活性。

## Slide 34: 阵列设计--接口优化技术
满足访存高速性：
采用DIMM互联
满足数据准确性：
采用“信号线+地线”设计
Notes: 子板FPGA与母板SOC的互联通道，采用DIMM形式实现，是原型系统中存储器访存的高速通道，数据翻转率高达140MHz。为保证高速通信下的数据准确性，在电路层面，我们采用50欧姆单端信号线，每根信号线在穿越DIMM物理接口时，配合接地信号线，确保参考平面的完整性；FPGA的IO选择 FAST模式，设定IO阻抗为50欧姆，实现阻抗匹配；在逻辑层面，采用输入输出引脚插入寄存器的方式，以流水线的策略降低后级逻辑的时序压力，确保FPGA内逻辑的高速运行。

## Slide 35: 创新点1：面向混合主存的离线任务分配算法设计
Designed in Lab
Notes: This is the platform developed with hybrid main memory architecture. The main board is a Zedboard with two DRAM chips. And the PCM board is connected to Zedboard with FMC interface. There are four PRAM chips on the board. The four chips are divided into two channels, each with two chips work in series.

## Slide 36: 方案说明
方案四：通用计算机环境中的统一内外存验证方案
Notes: 在通用计算机环境中验证统一内外存方案。

## Slide 37: 方案说明
方案五：基于Zynq的统一内外存SOC验证方案
Notes: 基于Zynq的芯片级ARM+FPGA实现统一内外存验证方案

## Slide 38: 延迟讨论
R1：ARM内核读指令传输至底板
FPGA的时间
R2：底板FPGA读指令传输至子板
FPGA的时间
R3：子板FPGA读操作传输至MRAM芯
片的时间
R4：MRAM芯片本征读时间
R5：子板FPGA获取MRAM芯片数据的
时间
R6：底板FPGA获取子板FPGA数据的
时间
R7：ARM内核获取底板FPGA数据的
时间
W1：ARM内核写指令传输至底板
FPGA的时间
W2: 底板FPGA写指令传输至子板
FPGA的时间
W3: 子板FPGA写操作传输至MRAM芯
片的时间
W4：MRAM芯片本征写时间
读时间=R1+R2+R3+R4+R5+R6+R7=140ns
写时间=W1+W2+W3+W4=90ns

## Slide 39
读时间：
R1+R2+R3+R4+R5+R6+R7=180ns
写时间：
W1+W2+W3+W4=110ns

## Slide 40
如何设计高性能CPU?
如何设计存储器系统？
如何设计I/O?

## Slide 41: 程序及指令的执行过程
程序和指令的关系
  程序由一条一条指令组成，指令按顺序存放在内存连续单元
程序的执行：周而复始地执行一条一条指令
  正常情况下，指令按其存放顺序执行
  遇到需改变程序执行流程时，用相应的转移指令（包括无条件转移指令、条件转移指令、调用指令和返回指令等）来改变程序执行流程
程序的执行流的控制
  将要执行的指令所在存储单元的地址由程序计数器PC给出，通过改变PC的值来控制执行顺序
指令周期：CPU取出并执行一条指令的时间

## Slide 42: 程序及指令的执行过程
CPU运行程序的过程就是执行一条一条指令的过程
CPU执行指令的过程中，包含CPU操作、访问内存或I/O端口的操作两类
访存或I/O：涉及存储系统、总线和I/O接口等内容（以后章节内容）
CPU内部操作：
涉及CPU内部数据通路（本章节内容）

## Slide 43: 机器指令的执行过程
CPU执行指令的过程
    取指令
    PC+“1”
    指令译码
    进行主存地址运算
    取操作数
    进行算术 / 逻辑运算
    存结果
    以上每步都需检测“异常”
    若有异常，则自动切换到异常处理程序
    检测是否有“中断”请求，有则转中断处理
指令执行过程
问题：
“取指令”一定在最开始做吗？PC+“1”一定在译码之前做吗？
“译码”须在指令执行前做吗？
异常是在CPU内部发生的，中断是由外部事件引起的
取指阶段
执行阶段
“1”：指一条指令的长度，定长指令字每次都一样；变长指令字每次可能不同
定长指令字通常在译码前做，变长指令字在译码后做！

## Slide 44: 机器指令的执行过程
取指令：从PC所指单元取出指令送指令寄存器（IR），并增量PC。
  如add函数，开始PC（IA-32的EIP）中存放的是0x0848394，CPU根据PC取指令送IR，每次总是取最长指令字节数，假定最长指令是4个字节，即IR为32位，此时，也即55 89 E5 8BH被取到IR中。
指令译码：不同指令其功能不同，因而需要不同的操作控制信号。
  CPU根据不同操作码译出不同控制信号。对于上述取到IR中的55 89 E5 8BH译码时，可根据高5位01010译码得到push指令的控制信号。
源操作数地址计算并取操作数：根据寻址方式确定源操作数地址计算方式，若是存储器数据，则需一次或多次访存；若为间接寻址或两操作数都在存储器的双目运算，则需多次访存；若是寄存器数据，则直接从寄存器取数。
执行数据操作：在ALU或加法器等运算部件中对取出的源操作数进行运算。
目的操作数地址计算并存结果：根据寻址方式确定目的操作数地址计算方式，若是存储器数据，则需要一次或多次访存（间接寻址时）；若是寄存器数据，则在进行数据操作时直接存结果到寄存器。
指令地址计算并将其送PC。顺序执行时，PC加上当前指令长度；遇到转移类指令时，则需要根据条件码、操作码和寻址方式等确定下条指令地址。

## Slide 45
指令是如何在各部件间执行（流动）的？
数据通路是道路
时序控制是警察

## Slide 46: 状态元件：时序逻辑电路
状态（存储）元件的特点：
  具有存储功能，在时钟控制下输入被写到电路中，直到下个时钟到达
  输入端状态由时钟决定何时被写入，输出端状态随时可以读出
定时方式：规定信号何时写入状态元件或何时从状态元件读出
  边沿触发（edge-triggered）方式：
    状态单元中的值只在时钟边沿改变。每个时钟周期改变一次。
      上升沿（rising edge） 触发：在时钟正跳变时进行读/写。
      下降沿（falling edge）触发：在时钟负跳变时进行读/写。
最简单的状态单元（回顾：数字逻辑电路课程内容）：
  D触发器：一个时钟输入、一个状态输入、一个状态输出
时钟周期
上升沿
下降沿
数据通路中的状态元件有两种：寄存器(组) + 存储器

## Slide 47
时钟信号（晶振与时钟发生器）
CUP频率（主频）
外频
分频和倍频（超频）
内存频率、前端总线（北桥）、I/O（南桥）
CPU的运算速度还要看CPU的流水线的各方面的性能指标

## Slide 48: 数据通路与时序控制
Clk
寄存器的输入可变化
Setup
Hold
.
.
.
.
.
.
.
.
.
.
.
.
Setup
Hold
数据通路由“ … + 状态元件 + 操作元件( 组合电路) + 状态元件 + …” 组成
只有状态元件能存储信息，操作元件须从状态元件接收输入，并将输出写入状态元件。其输入为前一时钟生成的数据，输出为当前时钟所用的数据
现代计算机的时钟周期
Clk
Clk
Notes: Remember, we will be using a clocking methodology where all storage elements are clocked by the same clock edge.
Consequently, our cycle time will be the sum of:
(a) The Clock-to-Q ( or latch propagation) time of the input registers.
(b) The longest delay path through the combinational logic block.
(c) The set up time of the output register.
(d) And finally the clock skew.
In order to avoid hold time violation, you have to make sure this inequality is fulfilled.
+2 = 18 min. (X:58)
Complements:
Why use edge-triggerd clocking methodology? simpler to explain in contrast to level-triggered.
Clock skew: difference in absolute time between the times when two state elements see a clock edge. It arises because the clock signal often follows different paths, with slightly delays, to reach two different state elements. Clock skew may cause a forward race of new inputs to the next flip-flop, leading to incorrect operation. (see Fig.B.31 at page B-41).
Clock-to-Q(or latch propagation): the propagation time of signal through a flip-flop from clock to the output Q. That is why it is called clock to Q time.
Setup time/hold time of flip-flop: the minimum time during which the input must be valid( or stable) before/after the clock edge.(page B-24)
(Latch Prop + Shortest Delay Path - Clock Skew) > Hold Time : this might be difficult to explain, but otherwise it will cause the race problem as shown in Fig.B.31.

## Slide 49: 操作元件：组合逻辑电路
加法器(Adder)
多路选择器 (MUX)
算逻部件(ALU)
32
A
B
32
Y
32
Select
MUX
32
32
A
B
32
Result
Zero
OP
ALU
32
32
A
B
32
Sum
Carry
Adder
CarryIn
3
Decoder
out0
out1
out7
out2
译码器(Decoder)
控制信号
组合逻辑元件的特点：
其输出只取决于当前的输入。即：若输入一样，则其输出也一样
定时：所有输入到达后，经过一定的逻辑门延时，输出端改变，并保持到下次改变，不需要时钟信号来定时
Notes: Based on the Register Transfer Language examples we have so far, we know we will need the following combinational logic elements.
We will need an adder to update the program counter.
A MUX to select the results.
And finally, an ALU to do various arithmetic and logic operation.
+1 = 30 min. (Y:10)

## Slide 50
如何提速？
流水线（假并行）
并行
超流水线
超长指令：减少访存
编译
超标量：动态多发

## Slide 51: 指令流水线的基本概念
五段流水线
取指令(IF)：根据PC的值从存储器取出指令。
指令译码(ID)：产生指令执行所需的控制信号。
取操作数(OF)：读取存储器操作数或寄存器操作数。
执行(EX)：对操作数完成指定操作。
写回(WB)：将操作结果写入存储器或寄存器。

## Slide 52: 单周期数据通路中指令的执行
假定：最复杂指令执行过程 ① 取指：200ps；②译码和读操作数：50ps；③ALU操作：100ps；④读存储器：200ps；⑤结果写寄存器：50ps。
200+50+100+200=600
单周期：每条指令在单个时钟周期内完成，故CPI=1，时钟周期=600ps
每秒执行指令条数：
1/600ps=1/(600×10-15)=1.67×1012
CPI=1，指令延时为600ps
指令吞吐率为1.67GIPS
指令串行执行，程序执行时间为：指令条数×600ps

## Slide 53: 流水线数据通路中指令的执行
假定：最复杂指令执行过程 ① 取指：200ps；②译码和读操作数：50ps；③ALU操作：100ps；④读存储器：200ps；⑤结果写寄存器：50ps。
取指令
译码/读数
ALU运算
读/写存储器
写结果
最长段为200ps
指令延时为：250ps×5=1.25ns
指令吞吐率为4GIPS

## Slide 54: 流水线指令集的设计
具有什么特征的指令集有利于流水线执行呢？
  长度尽量一致，有利于简化取指令和指令译码操作
    MIPS指令32位，下址计算方便: PC+4
    X86指令从1字节到17字节不等，使取指部件极其复杂
  格式少，且源寄存器位置相同，有利于在指令未知时就可取操作数
    MIPS指令的rs和rt位置一定，在指令译码时就可读rs和rt的值
    若位置随指令不同而不同，则需先确定指令类型才能取寄存器编号
  load / Store指令才能访问存储器，有利于减少操作步骤，规整流水线
    lw/sw指令的地址计算和运算指令的执行步骤规整在同一个周期
    X86运算类指令操作数可为内存数据，需计算地址、访存、执行
  内存中”对齐”存放，有利于减少访存次数和流水线的规整
  总之，规整、简单和一致等特性有利于指令的流水线执行
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 55: 按指令格式的复杂度来分
早期CISC设计风格的主要特点
(1) 指令系统复杂
变长操作码 / 变长指令字 / 指令多 / 寻址方式多 / 指令格式多
(2) 指令周期长
绝大多数指令需要多个时钟周期才能完成
(3) 各种指令都能访问存储器
除了专门的存储器读写指令外，运算指令也能访问存储器
(4) 采用微程序控制
(5) 有专用寄存器
(6) 难以进行编译优化来生成高效目标代码
例如，VAX-11/780小型机
  16种寻址方式；9种数据格式；303条指令；一条指令包括1～2个字节的操作码和下续N个操作数说明符。一个说明符的长度达1 ～10个字节。
按指令格式的复杂度来分，有两种类型计算机：
  复杂指令集计算机CISC (Complex Instruction Set Computer)
  精简指令集计算机RISC (Reduce Instruction Set Computer)

## Slide 56: 复杂指令集计算机CISC
对CISC进行测试，发现一个事实：
  在程序中各种指令出现的频率悬殊很大，最常使用的是一些简单指令，这些指令占程序的80%，但只占指令系统的20%。而且在微程序控制的计算机中，占指令总数20%的复杂指令占用了控制存储器容量的80%。
1982年美国加州伯克利大学的RISCⅠ，斯坦福大学的MIPS，IBM公司的IBM801相继宣告完成，这些机器被称为第一代RISC机。
CISC的缺陷
  日趋庞大的指令系统不但使计算机的研制周期变长，而且难以保证设计的正确性，难以调试和维护，并且因指令操作复杂而增加机器周期，从而降低了系统性能。
1975年IBM公司开始研究指令系统的合理性问题，John Cocks提出精简指令系统计算机 RISC ( Reduce Instruction Set Computer )。

## Slide 57: RISC设计风格的主要特点
(1) 简化的指令系统
指令少 / 寻址方式少 / 指令格式少 / 指令长度一致
(2) 以RR方式工作
除Load/Store指令可访存外，其余指令都只访问寄存器
(3) 指令周期短
以流水线方式工作， 因而除Load/Store指令外，其他简单指令都只需一个或一个不到的时钟周期就可完成
(4) 采用大量通用寄存器，以减少访存次数
(5) 采用硬连线路控制器，不用或少用微程序控制
(6) 采用优化的编译系统，力求有效地支持高级语言程序
MIPS是典型的RISC处理器，82年以来新的指令集大多采用RISC体系结构
x86因为“兼容”的需要，保留了CISC的风格，同时也借鉴了RISC思想

## Slide 58: 指令流水线的实现
假定：最复杂指令执行过程 ① 取指：200ps；②译码和读操作数：50ps；③ALU操作：100ps；④读存储器：200ps；⑤结果写寄存器：50ps。
取指令
IFetch
读数/译码
Reg/Dec
ALU运算
Exec
读/写存储器
Mem
写结果
Write
可以分5个流水段，最长阶段为200ps

## Slide 59: 指令流水线的执行举例
End of
Cycle 4
End of
Cycle 5
End of
Cycle 6
End of
Cycle 7
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Ifetch
Reg/Dec
Exec
Mem
Wr
0: Load
Ifetch
Reg/Dec
Exec
Mem
Wr
4: R-type
Ifetch
Reg/Dec
Exec
Mem
Wr
8: Store
Ifetch
Reg/Dec
Exec
Mem
Wr
12: Beq
周期4结束: Load 的 Mem, R-type 的 Exec, Store 的 Reg, Beq 的 Ifetch
周期5结束: Load 的 Wr, R-type 的 Mem, Store 的 Exec, Beq 的 Reg
周期6结束: R-type 的 Wr, Store 的 Mem, Beq 的 Exec
周期7结束: Store 的 Wr, Beq 的 Mem
考察以下几个点的情况：
Notes: Well, let’s look at a more complex example so I can show you how different instructions at different stages of execution can be processed by our pipelined datapath simultaneously.
Let’s consider the following instruction sequence: Load, R-type, Store, and then Branch on equal to target address 1000.
In the next four slides, I will show you the state of the datapath at the end of Cycle 4, Cycle 5, Cycle 6 and Cycle 7.
First let’s take a look at the end of Cycle 4 where:
(a) The Load instruction has just finished its Mem stage.
(b) The R-type instruction has just finished its Exec stage.
(c) The Store instruction has just finished its Register Fetch slash Instruction Decode stage.
(d) And finally, the Branch instruction has just finish fetching the instruction.
Remember now, the next four pictures we will be looking at are at the end of a clock cycle. That is right at the clock tick.
+2 = 59 min. (Y:39)

## Slide 60: 指令流水线的执行举例
lw指令与beq、sub、or指令关于$8数据相关
sub与or关于$9数据相关
可通过转发解决数据相关
可通过前半周期写后半周期读解决数据相关
Load-use数据相关不能通过转发解决
指令lw与beq是load-use数据相关

## Slide 65
Hazards：指流水线遇到无法正确执行后续指令或执行了不该执行的指令
  结构冒险 (hardware resource conflicts，硬件资源冲突):
  现象：同一个部件同时被不同指令所使用
    一个部件每条指令只能使用1次，且只能在特定周期使用
    设置多个部件，以避免冲突。如指令存储器IM 和数据存储器DM分开
  数据冒险 (data dependencies，数据相关):
  现象：后面指令用到前面指令结果数据时，前面指令的结果还没产生
    转发(Forwarding/Bypassing旁路) 或 前半周期读后半周期写
    Load-use冒险不能通过转发解决，需阻塞(stall)一个时钟周期
    编译程序优化指令顺序
  控制 (分支) 冒险 (changes in program flow，改变控制流):
  现象：转移或异常改变执行流程，后继指令在目标地址产生前已被取出
    采用静态或动态分支预测
    编译程序优化指令顺序(分支延迟)
流水线的冲突/冒险(hazard)情况
1、就当没做
2、就是没做
3、做点其他

## Slide 66: 编译器优化指令顺序解决数据冒险
以下源程序可生成两种不同的代码，优化的代码可避免Load阻塞
a = b + c;
d = e – f;
假定 a, b, c, d ,e, f 在内存
Fast code:
lw $2, b
lw $3, c
lw $5, e
add $1, $2, $3
lw $6, f
sw $1, a
sub $4, $5, $6
sw $4, d
Slow code:
lw $2, b
lw $3, c
add $1, $2, $3
sw $1, a
lw $5, e
lw $6, f
sub $4, $5, $6
sw $4, d
调整后
编译器的优化很重要！
如果硬件不支持阻塞处理的话，则编译器可以将顺序调整和插入NOP指令结合起来，在找不到可插入的指令时，插入NOP指令！

## Slide 67: 编译器优化以避免阻塞的情况调查
由此可见，优化调度后load阻塞现象大约降低了1/2~1/3

## Slide 68: 编译器优化指令顺序解决控制冒险
基本思想：把分支指令前面的与分支指令无关的指令调到分支指令后面执行，以填充延迟时间片（也称分支延迟槽Branch Delay slot），不够时用nop填充
如何对以下程序段进行分支延迟调度？（假定时间片为2）
调度后，无需在硬件线路中阻塞branch指令后面指令的执行
lw $1, 0($2)
lw $3, 0($2)
add $6, $4, $2
beq $3, $5, 2
add $3, $3,$2
sw $1, 0($2)
……
调度后可能带来其他问题：产生新的load-use数据冒险
调度后
lw $3, 0($2)
add $6, $4, $2
beq $3, $5, 2
lw $1, 0($2)
nop
add $3, $3,$2
sw $1, 0($2)

## Slide 69: 本章小结
CPU的基本功能是周而复始地执行指令，并处理异常和中断。
CPU最基本的部分是数据通路和控制单元
  数据通路（datapath）中包含组合逻辑元件和存储信息的状态元件。
    组合逻辑（如加法器、ALU、扩展器、多路选择器以及状态元件的读操作逻辑等）用于对数据进行处理；
    状态元件包括触发器、寄存器和存储器等，用于对指令执行的中间状态或最终结果进行存储。
  控制单元（control unit）：对取出的指令进行译码，与指令执行得到的条件标志或当前机器的状态、时序信号等组合，生成对数据通路进行控制的控制信号。
指令执行过程主要包括取指、译码、取数、运算、存结果。
现代计算机的数据通路都采用流水线方式实现，将每条指令的执行过程分解成功能段相同的几个流水段。流水线方式下，同时有多条指令重叠执行，因此程序的执行时间比串行执行方式下缩短很多。